## Slide 1: Status of work
Ondrej Pavlas

## Slide 2
Debugging problem with Timepix2
Katherine
For
Timepix2
Chipboard
with
Timepix2
Conversion
board
Setup:
Reading basic registers : OK
Reading 4-bits counters (D,C) : OK
Problem:
Reading 10 – bits counter (A, B): Problem with one column of pixels -> unable to connect to Katherine

## Slide 3
Debuging problem with Timepix2
Katherine
For
Timepix2
Hardpix
Chipboard
with
Timepix2
Conversion
board
Setup:
UWB
Chipboard
with
Timepix2

## Slide 4
Základní
deska
Deska s Timepix2
PCB
Uživatel
(PC)
USB
Mikrokontrolér
Napájení
Konverze log. úrovní
USB
Timepix 2
Napájení
HV zdroj
Měření teploty

## Slide 5
+5V
USB-C
+3V3
+2V5
EN_2V5
+1V2
EN_1V2

## Slide 6
Nastavení rozlišení senzoru na 12 bitů
Výběr registru senzoru, kde je uložená informace o teplotě
Převod teploty na desetiné číslo
Vyčtení teploty
Uživatelský příkaz
Teplota na desce s Timepix 2

## Slide 7
Working on diploma thesis
Mini readout for Timepix2
PCBs:
Mainboard
Chipboard
TOP
TOP
BOT
BOT

## Slide 8
Working on diploma thesis
Mini readout for Timepix2
Properties of device:
Interface: USB - type C
Comm. speed : USB High Speed: 480 Mbps
Timepix2 readout speed : up to 50 MHz
HV source: 30 – 150 V
Power consumption low as possible: first test -> 350 mW
MCU : STM32U5A9 : Arm Cortex-M33
    RAM: 2.44MB, Flash: 4MB, 160 Mhz
Dimension of device : 70 x 20 x 15 mm

## Slide 9
Working on diploma thesis
Mini readout for Timepix2
Progress:
Digital test of Timepix2: OK
USB : Virtual COM port: OK
HV: OK
TODO:
Connect to TrackLab
Housing
Thanks to:
Milan Malich, Pavel Skoták,
Michael Holík, Martin Oblrich,
Petr Burian, Petr Smolyanskiy

## Slide 10
Working on diploma thesis
Mini readout for Timepix2
Testing of chipboard:
Katherine
For
Timepix2
Chipboard
with
Timepix2
Conversion
board
After first test looks OK

## Slide 11
Thanks for your attention